## Slide 1: A first glance of DVB-I over 5G: DVB-MABR over LTE-based 5G Broadcast
Thomas Stockhammer, Romain Bouqueau, Christophe Burdinat
  Qualcomm Incorporated jointly with ATEME, Viaccess-Orca and Motion Spell
DVB Demos
September 30, 2021
@qualcomm

## Slide 2: DVB-I Service Layer for
Non-5G
IP/HTTP Network
DVB-I over 5G Commercial Require- ments completed in July 2021
5G Release-16 means
  LTE-based 5G Broadcast
  Unicast-based 5G Media Streaming
  Hybrid services
Service Layer based on DVB-I
  DVB-AVC codecs
  DVB-DASH incl Low-Latency DASH + CMAF
  DVB-MABR: ABR Multicast including ROUTE
  DVB-I Service Layer
Technical work has started in DVB
This is a first glance
5G Broadcast
System
BCAST (ENTV)
Unicast (NR)
5G Operator with 5G Media Streaming
5GC
BMSC
DVB-I client (DVB-I metadata, DVB-Codecs, DVB-DASH, DVB-MABR)
M6d
M7d
MBMS-API
DVB-I Headend (DVB-AVC, DVB-DASH, DVB-MABR, DVB-I)
xMB
M1d/M2d
Notes: 45s

## Slide 3: FFFocus of this demo
Feasibility
  Reception of "DVB-I over 5G live broadcast-signal" on 5G mobile device
Functionality
  Basic broadcast distribution of DVB-DASH content
  Low-latency distribution using LL-DASH/CMAF and ROUTE
  Seamless broadcast coverage extension with unicast fall-back
Future-proof
  Off-the shelf tools: commercial phones, stock DVB-DASH players, etc.
  Open source: dash.js, GPAC ROUTE, etc.
A first glance of DVB-I over 5G
Notes: 45s

## Slide 4: Demo 1: Feasibility
DVB-I over LTE-based 5G Broadcast
DVB-AVC
DVB-DASH
Live
DVB-MABR
ROUTE Server
LTE-based 5G Broadcast Transmitter
LTE-based 5G Broadcast receiver
DVB-MABR
ROUTE Client
DVB-DASH and AVC
Client
LTE enTV radio bearer
OnePlus 9
Notes: 120s

## Slide 6: Demo 2: Functionalities
Low-Latency & Hybrid Service Continuity
DVB-AVC
DVB-LL-DASH
Live
DVB-MABR
LL-ROUTE Server
DVB-MABR
ROUTE Gateway
DVB-LL-DASH & AVC
Client
LTE-based 5G Broadcast Emulator
5G System
Media Streaming unicast
Smart Gateway
Notes: 120s

## Slide 8: Future
Available Open Source Tools
  To be added GPAC, dash.js, Akamai source
Next Steps
  Combination of feasibility and functionalities
  Adding additional functionalities
  Integration into 5G-MAG Reference Tools
For more details on setup and command lines, please contact us or join us in the afternoon
Notes: 30s